## Slide 1: Project 6
Unicast DHCP Application
Date: | 2019/05/09 (Thu.)
Deadline: | 2019/05/26 (Sun.)

## Slide 2: Outline
About DHCP
Project 6 Requirements
Hints

## Slide 3: Outline
About DHCP
Project 6 Requirements
Hints

## Slide 4: About DHCP (1/8)
Dynamic Host Configuration Protocol
  Provide necessary information for a host to access network
    IP address, gateway, DNS (Domain Name Server), etc.
  A DHCP transaction is completed by 4-way handshake:
client
server
DISCOVER
OFFER
REQUEST
ACK
unicast
broadcast
time

## Slide 5: About DHCP (2/8)
Notes: 實際的例子

## Slide 6: About DHCP (3/8)
switch
DHCP
server
host 1
host 2
newly attached,
interface is configured as DHCP

## Slide 7: About DHCP (4/8)
DHCP DISCOVER (L2 broadcast)
L2
Src.:HOST1_MAC
Dst.:FF:FF:FF:FF:FF:FF
L3
Src.:0.0.0.0
Dst.:255.255.255.255
DHCP DISCOVER
switch
DHCP
Server
10.1.11.3/24
host 1
host 2

## Slide 8: About DHCP (5/8)
DHCP OFFER (unicast)
DHCP OFFER
L2
Src.:SERVER_MAC
Dst.:HOST1_MAC
L3
Src.:10.1.11.50
Dst.:10.1.11.102
IP for
host 1
switch
DHCP
Server
10.1.11.3/24
host 1
host 2

## Slide 9: About DHCP (6/8)
DHCP REQUEST (L2 broadcast)
L2
Src.:HOST1_MAC
Dst.:FF:FF:FF:FF:FF:FF
L3
Src.:0.0.0.0
Dst.:255.255.255.255
DHCP REQUEST
switch
DHCP
Server
10.1.11.3/24
host 1
host 2

## Slide 10: About DHCP (7/8)
DHCP ACK (unicast)
DHCP ACK
L2
Src.:SERVER_MAC
Dst.:HOST1_MAC
L3
Src.:10.1.11.50
Dst.:10.1.11.102
switch
DHCP
Server
10.1.11.3/24
host 1
host 2

## Slide 11: About DHCP (8/8)
switch
DHCP
Server
10.1.11.3/24
host 1
10.1.11.26/24
host 2
10.1.11.25/24

## Slide 12: Outline
About DHCP
Project 6 Requirements
Hints

## Slide 13: Project 6 Requirement
In this project, you need to implement an unicast DHCP application that support:
  Dynamically set DHCP server’s connect point through REST API (configuration service).
  Compute path between DHCP client and DHCP server.
  Install flow rules to forward DHCP transaction traffic.
switch 1
switch 2
DHCP
server
host 2
host 1
May I have an IP address?
Notes: Configuration service mentioned here will be explained later.
In function 2, “DHCP server” here means the connect point specified in configuration file.

## Slide 14: Project 6 Requirement - Workflow (1/7)
Before DHCP transaction
  Network manager upload configuration file to ONOS
  Your application should install a flow rule to request DHCP packets
DHCP DISCOVER will be packet-in to controller by switch
Controller compute path between DHCP client and server
Controller install flow rules to forward DHCP packets
Done
Notes: Can skip this page

## Slide 15: Project 6 Requirement - Workflow (2/7)
Unicast DHCP
Controller
DHCP server: of:0…02/1
1. JSON file
2. REST API (POST)
3. DHCP server is at
of:0…02/1
a. Network manager upload configuration file to ONOS
Notes: Configuration service mentioned here will be explained later.

## Slide 16: Project 6 Requirement - Workflow (3/7)
switch 1
switch 2
DHCP
server
host 2
host 1
Controller
Unicast DHCP
Install flow rule to
request DHCP packets.
data plane
control plane
b. Your application should install a flow rule to request DHCP packets
Send all DHCP packet to me if I haven’t tell you how to forward them.

## Slide 17: Project 6 Requirement - Workflow (4/7)
switch 1
DHCP DISCOVER (L2 broadcast)
switch 2
DHCP
server
host 2
host 1
Controller
Unicast DHCP
data plane
control plane
DHCP DISCOVER will be packet-in to controller by switch

## Slide 18: Project 6 Requirement - Workflow (5/7)
switch 1
switch 2
DHCP
server
host 2
host 1
Controller
Unicast DHCP
data plane
control plane
Controller compute path between DHCP client and server
(Note: a bit like what you did in project 4)

## Slide 19: Project 6 Requirement - Workflow (6/7)
switch 1
switch 2
DHCP
server
host 2
host 1
Controller
Unicast DHCP
data plane
control plane
Controller install flow rules to forward DHCP packets
(Note: proactive and reactive forwarding are both acceptable)
Install flow rule to
forward DHCP packets
between host 1 and server

## Slide 20: Project 6 Requirement - Workflow (7/7)
switch 1
switch 2
DHCP
server
host 2
host 1
Controller
Unicast DHCP
data plane
control plane
Done
Here’s the IP address!
Nice, I’ll take it.
Thanks.

## Slide 21: Project 6 Requirement - Provided File
“project_6.zip” includes two directories and following files:
  EchoConfig: (reference for ONOS users)
    EchoConfig is an example application that read configuration file through REST API and echo it to log file.
    Sample configuration file is also provided.
    This application is provided with ONOS version only.
  SDN-NFV-Project6:
    topo.py: mininet topology
    dhcpd.conf: configuration file for mininet topology
    unicastdhcp.json: configuration file for unicast DHCP app (example for ONOS users)
Notes: Sample application that introduce configuration service.
Contains files that are necessary for you to complete project 6

## Slide 22: Project 6 Requirement - Topology
The topology provided in ”project_6.zip” consist of:
  3 switches
  3 hosts
  1 DHCP server
h4
(DHCP server)
10.1.11.3/24
h3
h2
h1
s1
s3
s2
Notes: In this project, we want you to run your unicast DHCP application so that h1, h2, h3 in this topology can get IP from DHCP server.

## Slide 23: Project 6 Requirement - Commands (1/2)
Remember to install isc-dhcp-server before you start this project:
To use dhcpd, we should disable/modify AppArmor (only need to be done in the first time)
$ sudo apt-get install isc-dhcp-server
$ sudo ln -s /etc/apparmor.d/usr.sbin.dhcpd /etc/apparmor.d/disable/ $ sudo apparmor_parser -R /etc/apparmor.d/usr.sbin.dhcpd
sudo /etc/init.d/apparmor stop sudo sed -i '30i /var/lib/dhcp{,3}/dhcpclient* lrw,' /etc/apparmor.d/sbin.dhclient sudo /etc/init.d/apparmor start

## Slide 24: Project 6 Requirement - Commands (1/2)
Use following command to start the topology:
In mininet CLI, use following command to ask an IP for a host
(which means to start an DHCP transaction):
H1 –eth0
$ sudo python topo.py
mininet> h1 dhclient {interface_name}

## Slide 25: Project 6 Requirement - Configuring
Use following command to upload a config file by REST API:
  For ONOS:
  For RYU:
    https://osrg.github.io/ryu-book/zh_tw/html/rest_api.html
$ onos-netcfg {controller_IP} {json_file_name}

## Slide 26
app deactivate fwd
tools/test/bin/onos localhost
cd $ONOS_ROOT/tools/package/archetypes/app
onos-app localhost reinstall! target/app-1.0-SNAPSHOT.oar
$ mvn clean install -DskipTests
onos-netcfg 127.0.0.1 unicastdhcp.json
h1 dhclient h1-eth0
http://localhost:8181/onos/ui

## Slide 27: Submit to e3
Files
  All files of your application
  Config file you used in provided topology
Submit
  Upload “.zip” file to e3
    Named: project6_studentID.zip
  Wrong file name or format would not be scored

## Slide 28: Outline
About DHCP
Project 6 Requirements
Hints
  EchoConfig

## Slide 29: Hints - EchoConfig
EchoConfig is an example application that read configuration file through REST API and echo it to log file.
We will explain this application for ONOS and RYU separately.
EchoConfig
Controller
JSON
1. JSON file
2. REST API (POST)
3. Print on log

## Slide 30: Project 6 Requirement - Workflow (2/7)
Unicast DHCP
Controller
DHCP server: of:0…02/1
1. JSON file
2. REST API (POST)
3. DHCP server is at
of:0…02/1
a. Network manager upload configuration file to ONOS
Notes: Configuration service mentioned here will be explained later.

## Slide 31: Hints – EchoConfig ONOS version (1/2)
Including:
  2 source code files
    AppComponent.java: main source code file for the application
    MyConfig.java: the config class which will be imported in
    “AppComponent.java”.
  1 sample config file
Create your own EchoConfig application according to provided source code.
  You may need to do some modification according to your package name.
Compile your application and install into ONOS

## Slide 32: Hints – EchoConfig ONOS version (2/2)
Check that the application title is correct in configuration file:
Upload the config file
The EchoConfig application will echo the config file in ONOS log: