## Slide 1: Lab 3 Recall
Packet-out defined in OpenFlow 1.3
Make sure to Packet-out when you send Flow-mod
  Since flow modification message only install flow rule on the switch
  … without buffer ID
Flow modification messages with buffer ID
Refer from OpenFlow specification v1.3.0

## Slide 2: Project 4
Path Service
Date: | 2019/04/11 (Thu.)
Deadline: | 2019/04/28 (Sun.)

## Slide 3: Ryu – What Should an SDN Application do?
Request Packet-in
  switch_features_handler()
Handle Packet-in
  _packet_in_handler()
Packet-out
  OFPPacketOut()
Flow-mod
  add_flow() // OFPFlowMod()
Refer from Ryu SimpleSwitch13

## Slide 4: ONOS – What Should an SDN Application do?
Request Packet-in
  requestIntercepts()
Handle Packet-in
  PacketProcessor{process()}
Packet-out
  packetOut() // PacketContext.setOutput().send()
Flow-mod
  installRule() // FlowObjectiveService.forward()
Refer from ONOS v1.15 ReactiveForwarding

## Slide 5: Outline
Project 4 Requirements
Reference

## Slide 6: Outline
Project 4 Requirements
Reference

## Slide 7: Project 4 Requirements
Path Service
Notes: 說明有兩種方式 CLI AND restful api

## Slide 8: Requirement
Write a path service application which finds a path
  Construct a graph of network topology when Packet-in
  Find a path between the source and destination
  You could use algorithms like BFS, Dijkstra or spanning tree
  Shortest path algorithms are not required
Proactive install flow rules on each devices in the path
  Each packet from hosts would only trigger one Packet-in
  Flow rules would be proactively installed on devices in the following path
  Compare with reactive forwarding such as SimpleSwitch13 in Ryu or ReactiveForwarding in ONOS

## Slide 9: Write ONOS Application
You code should be placed under `src/main/java/nctu/winlab/testapp/`
A template code is created , and you can simply use it
$ cd <artifactId>
$ vi src/main/java/nctu/winlab/testapp/AppComponent.java

## Slide 10: Compile, Install and Activate ONOS Application
Compile ONOS application
Run ONOS
Install and activate ONOS application
Note: By using an exclamation mark with `install` parameter, the application will be activated immediately after being installed
$ cd <artifactId>
$ mvn clean install -DskipTests
$ ok clean
$ onos-app localhost reinstall! target/<package>-<version>.oar

## Slide 11
app deactivate fwd
tools/test/bin/onos localhost
cd $ONOS_ROOT/tools/package/archetypes/app
onos-app localhost reinstall! target/app-1.0-SNAPSHOT.oar
$ mvn clean install -DskipTests
http://localhost:8181/onos/ui

## Slide 12: Demonstration (I)
Using Mininet tree topology with depth in 2
$ sudo mn --controller=remote --topo=tree,depth=2

## Slide 13: Demonstration (II)
Ping from h1 to h3
ONOS log
  Only devices connected source hosts would send Packet-in
  Flow rules would be installed on devices in the following path
mininet> h1 ping h3

## Slide 14: Demonstration (III)
Capture OpenFlow packets from Loopback interface
Each ICMP request and reply only trigger one Packet-in

## Slide 15: Demonstration (IV)
Forwarding packets in data plane is much faster than installing flow rules in controller plane
Pingall in Mininet only take one ICMP packet into consideration
  Thus, pingall would not work
  Use ping to test your program
Refer from GitHub mininet/mininet - mininet/net.py

## Slide 16: Hints
Since forwarding packets in data plane is much faster than installing flow rules in controller plane
Install flow rules on network devices from destination to source in the path
Do not Packet-out when installing flow rules
  Or the packet which triggers Packet-in would reach the next device before the flow rule successfully installed
  The first packet is inevitably lost due to timeout
    That is why always two packet loss in every ping

## Slide 17: Outline
Project 4 Requirements
Reference

## Slide 18: Reference
Path Service
Notes: 說明有兩種方式 CLI AND restful api

## Slide 19: Reference
Ryu
  Ryu API Reference
    https://ryu.readthedocs.io/en/latest/api_ref.html
  Ryu GitHub – ryu/ryu/topology/api.py
    https://github.com/osrg/ryu/blob/master/ryu/topology/api.py
ONOS
  ONOS Java API 1.15.0
    http://api.onosproject.org/1.15.0/apidocs/
  ONOS TopologyService.getGraph() would return the topology graph
  DO NOT use ONOS built-in APIs to find paths (e.g. TopologyService.getPath())

## Slide 20: Submit to e3
Files
  All files of your application
Submit
  Upload “.zip” file to e3
    Named: project4_studentID.zip
  Wrong file name or format would not be scored

## Slide 21: Hints for Demo Scenario
Finding paths
  Your application should be able to deal with loops in the topology
Proactive installing flow rules
  Please check if only two Packet-in are captured from Wireshark instead of logging
    Since controller like ONOS would abstract some operations below
  Probably do not set timeout too short in case that switches trigger another Packet-in after flow rules timeout

## Slide 22: Thank you
Q & A